## Slide 1: Computational Haptics Labratory Final Project Presentation
Naina Dhingra, Ke Xu, Hannes Bohnengel
Technical University of Munich
TUM Department of Electrical and Computer Engineering
Chair of Media Technology
Munich, 08 August 2017

## Slide 2: Agenda:
Motivation of the Haptics Showroom
Software Implementation
Hardware Implemetation
Task mapping
Future work
Haptics Showroom demonstration
Haptics Showroom

## Slide 3: Motivation of Haptics Showroom
Great introduction to haptics in general (especially for newbies)
Enable user to walk through the room and interact with different haptic experiences within one virtual room.
Enable successors for the continued perfection of our haptics showroom effortlessly.
Haptics Showroom

## Slide 4: Creating an Environment
Creating the room
  Making the walls
  Making the floor and the ceiling
Creating 3ds objects
  Taking two dimensional objects and converting them to 3ds model.
  Creating different mesh objects. Mesh objects may be translated, rotated, or resized, and have one material and texture property assigned to them
  Creating different objects to experience the haptic effect of different textures and of varied temperature
  3ds objects help to experience a feel of reality (compared to 2D objects)
Haptics Showroom

## Slide 5: Haptics Showroom
Texture objects
Haptics Showroom
Temperature objects

## Slide 6: Software Implementation
Functions
void checkBoundaries();
int checkTempRegions();
void drawCoordinates(cVector3d position, double length, double width);
int newPlane(cVector3d position, MyProperties properties);
int newObjectcMesh(cVector3d position, MyProperties properties);
int newObjectcMultiMesh( cVector3d position, MyProperties properties,
string objectFile, double scalingFactor);
Haptics Showroom
Notes: Function to create planes with enabled force feedback (walls, floor)
Function to check if boundaries of room are violated when walking
Function which draws karteesian coordinates at some position
Function to create haptic objects at run time
Function to check the temperature region of the objects

## Slide 7: Software Implementation
Global variables
vector<cMesh*> object(MAX_OBJECT_COUNT);
int objectCounter = 0;
vector<cMultiMesh*> object3ds(MAX_OBJECT_COUNT);
int object3dsCounter = 0;
vector<MyRegions*> tempRegion(MAX_REGIONS_COUNT);
int tempRegionCounter = 0;
vector<cAudioBuffer*> audioBuffer(MAX_AUDIOBUFFER_COUNT);
int audioBufferCounter = 0;
Haptics Showroom

## Slide 8: Software Implementation
Classes
Haptics Showroom
MyRegions
+ MyRegions(…)
+ ~MyRegions(void)
+ position: cVector3d
+ size: cVector3d
+ temperature: int
- id: static int
MyProperties
+ MyProperties(…)
+ ~MyProperties(void)
+ textureImage: string
+ normalImage: string
+ audio: string
+ size: cVector3d
+ orientation: MyOrientation
+ shape: MyShape
+ temperature: int
+ stiffness: double
+ staticFriction: double
+ dynamicFriction: double
+ textureLevel: double
+ audioGain: double
+ audioPitchGain: double
+ audioPitchOffset: double
- id: static int

## Slide 9: Hardware Implementation
Haptics Showroom
Arduino Nano
Computer
Oculus Rift
Audio
Amplifier
Phantom
Omni
Switching Circuit
Voice Coil
Peltier
Element
Power Supply
Controller Box
Tool Adapter
(optional)

## Slide 10: Hardware Implementation
Voice coil
inside
Haptics Showroom
Phantom Omni and Tool Adapter
Peltier element

## Slide 11: Hardware Implementation
Haptics Showroom
Controller Box
Arduino Nano
Audio Amplifier
Switching Circuit

## Slide 12: Task mapping
SW:
Design of the room (floor, walls, ceiling, labels, walking functionality)
Audio stuff
Arduino control (SW + Interface in Visual Studio)
3ds objects (tables)
Classes (MyProperties, MyTempRegions)
MyObjectDatabase
Oculus support optional
HW:
Audio amplifier
Recording of sound files (for voice coil)
Peltier control (switching circuit)
Controller Box (putting it all together)
Haptic device adapter (Peltier and voice coil)
Ke, Hannes, Naina
Ke, Hannes
Hannes
Ke, Hannes, Naina
Hannes
Ke, Hannes
Ke, Hannes
Ke, Hannes
Ke
Hannes
Hannes
Ke, Hannes
Haptics Showroom

## Slide 13: Task mapping
Haptics Showroom
Task | Contributing Students |  | 
Designing the room (floor, walls, ceiling, labels, walking) | Naina | Hannes | Ke
Implementing Audio playback functionality |  |  | Ke
Implementing Arduino control (control SW + Interface in C++) |  | Hannes | 
Introducing 3ds objects | Naina | Hannes | Ke
Creating custom classes (MyProperties, MyTempRegions) |  | Hannes | 
Creating custum object database (MyObjectDatabase) |  | Hannes | Ke
Implementing Oculus support as optional |  | Hannes | Ke
Recording sound files (for voice coil) |  |  | Ke
Building Peltier control (switching circuit) |  | Hannes | 
Building controller box (cabling and assembly) |  | Hannes | 
Building haptic device adapter (Peltier and voice coil) |  | Hannes | Ke
SW
HW

## Slide 14: Future work
  Apply texture to 3ds objects
  Improve voice coil usage (not only scraping but also impact)
  Support multidevice usage
  Improve Peltier controller SW (exact temperature regulation)
  Introduce moving objects (with ODE)
  Introduce fixed objects (with 1 DoF)
Haptics Showroom

## Slide 15: Haptics Showroom Demonstration
Insert Video
Haptics Showroom